## Slide 1: Information Gathering and Reconnaissance
Notes: Firewall

## Slide 2: Hacking Stages
Information Gathering/Reconnaissance
Getting Access
Maintaining Access
Clearing Tracks

## Slide 3: What is Reconnaissance ?
Before launching an attack, skilled computer attackers often try to learn as much as possible about:
  The target systems and networks
    Hardware and software
    Topology
    Typical operation
  Administrators, Users, Owners

## Slide 4: Reconnaissance Steps
Reconnaissance can be divided in two steps:
  Step 1 – Intelligence gathering about the victim
    Open-source information: webpage, business partners, search engines etc.
    Social Engineering
    Physical Break-ins
    Dumpster Diving
  Step 2 – Intelligence gathering about the system
    There are scanning tools available to automatically scan:
      Hosts
      Network devices
      Services
      Vulnerabilities
Notes:   - bank robber example

## Slide 5: Step 1
Identifying url, IP addresses, and sub-domains
  Usually one of the first steps, it is important to identify the ip ranges and sub-domains associated with your target(s).
Identifying People
  Identifying names, email addresses, phone numbers and other personal information that can be valuable for phishing or other social engineering activities.
Identifying Technologies
  Identifying the types and versions of the systems and software applications in use by organization is an important precursor to identifying potential vulnerabilities.
Methods
  Browsing company web site
  Googling
  Use automated tools

## Slide 6: Practice 1
theHarvester - a tool for gathering e-mail accounts, user names and hostnames/subdomains from different public sources like search engines and PGP key servers
Download: https://github.com/laramies/theHarvester
Gather information about cse.usf.edu using theHarvester
  Unzip: unzip theHarvester-master.zip
  View theHarvester options: python theHarvester.py
Notes:   tar xvf theHarvester-XX.tar.gz

## Slide 7: Practice 1
theHarvester (unzip: unzip theHarvester-master.zip)
  View options: python theHarvester.py
  Full harvest on cse.usf.edu:
  python theHarvester.py -d cse.usf.edu -l 1000 -b bing
  Used options (flags):
    d: Domain to search or company name
    b: Data source (google, bing, bingapi, pgp, linkedin, google- profiles,people123,jigsaw,all)
    l: Limit the number of results

## Slide 8: Maltego
Maltego, open-source intelligence and forensics software developed by Paterva
Comprehensive GUI with relational graph
Advanced framework, allows customized plugins
Use big data and social network to analyze real-world relationships between people, websites, domain, networks, internet infrastructure, etc.
Notes: http://mtg-bi.com/

## Slide 9: Practice 2
Use Maltego to analyze cse.usf.edu network structure
  Start Maltego from menu
  Following registration wizard
    username: cdcusf@gmail.com
    Password: password
  Drag a domain entity and start explore!
What kind of information can we get?
Notes:   Download soctialnet from http://packetninjas.net/tools/socialnet.html

## Slide 10: Network Scanning
Scan a network to determine:
  Live hosts
  Network topology
    “Important” hosts
    Routers
    Firewalls
    Intrusion Detection Systems
  OSes
  Ports (services) open
  Vulnerabilities

## Slide 11: Nmap
Well-known port scanner, ping sweep and OS fingerprinting tool
Available for Linux, OS X and Windows:
  http://www.insecure.org/nmap/
Nmap and Zenmap (the graphical front end) are available in several versions and formats
Notes: Scan methods: http://www.auditmypc.com/port-scanning.asp

## Slide 12: Nmap Scans
Ping sweeps
  Example: nmap –sP target_ip
TCP connect
  Three-way handshake
  Example:
    nmap [-sT] target_ip
UDP
  Send a UDP packet
  Example:
    nmap –sU target_ip

## Slide 13: TCP/IP
In TCP/IP services are referenced using two components: an IP address and a port number
There are 65536 distinct ports
A request of service on a port generally falls into one of three categories:
  Open: the host responds to your request indicating a service is listening on the port
  Closed: the host responds but denies the request
  Blocked: there is no reply

## Slide 14: Port Scanning – TCP mode
Connect scan (completes the TCP three-way handshake)
  Send a TCP SYN segment to a target port
  If a SYN-ACK is returned
    The port is open
    Complete the three-way handshake with an ACK
    Terminate the connection with a FIN
  If no response, a RST, or an ICMP Port Unreachable is returned
    The port is closed
Unlikely to cause any problems on scanned host
Downside: Usually very easy to detect

## Slide 15: Port Scanning – UDP mode
There is no three-way handshake and no sequence numbers
  Send an ICMP packet to a target port
  If an ICMP Port Unreachable is returned
    The port is closed
  If no response is returned
    Assume the port is open or blocked
Downside :
  Easy to detect
  Unreliable
  Can be very slow when outgoing ICMP messages are rate-limited

## Slide 16: Nmap Scans – TCP SYN mode
Three-way handshake is not completed
  Sends SYN
  Awaits SYN-ACK
  Instead of final ACK, send RST or nothing
Example:
  nmap [-sS] target_ip
Slightly stealthy

## Slide 17: Nmap Scans – TCP FIN mode
Send a TCP FIN to a target port (violation of the TCP specification):
  If a RST is returned
    The port is closed
  If no response is returned
    The port may be open
Example:
  nmap [-sF] target_ip
More stealthy
Note: Will not work on Microsoft systems which do not follow the standard
Notes: TCP Protocol says that if somebody sends a FIN packet to a port that they haven’t already opened a connection on, then you have to send a RST back.

## Slide 18: Nmap Scans – Xmas Tree mode
Send a TCP segment to a target port with FIN, URG, and PSH code bits set (violation of the TCP specification)
  If a RST is returned
    The port is closed
  If no response is returned
    The port may be open
Example:
  nmap [-sX] target_ip
Note: Will not work on Microsoft systems which do not follow the standard
Notes: https://en.wikipedia.org/wiki/Christmas_tree_packet

## Slide 19: Nmap Scans – Null mode
Send a TCP segment to a target port with no flags set (violation of the TCP specification)
  If a RST is returned
    The port is closed
  If no response is returned
    The port may be open
Example:
  nmap [-sN] target_ip
More stealthy
Note: Will not work on Microsoft systems which do not follow standard

## Slide 20: Nmap Scans – TCP ACK mode
Send a TCP ACK to a target port (violation of the TCP specification)
  If a RST is returned
    The packet made it through the filter
    The port is unfiltered (established connections allowed)
  If no response or ICMP Port Unreachable is returned
    The packet didn’t make it through the filter (e.g. firewall blocked the packet)
    The port is filtered
Example:
  nmap [-sA] target_ip
Could be used to determine what rules a packet filter applies
Notes: Works for stateless firewalls (ex. built-in Windows firewall)
Iptables is a stateful firewall.

## Slide 21: Nmap Scans – other options
Specifying port ranges
  Scan only selected ports with the –p flag
Setting source ports
  Set source port (e.g. 80 or 25) so that the packets won’t be blocked (hopefully)
Using decoys
  Obscure the source of scans by sending decoy packets with a decoy source address

## Slide 22: Practice 3
Scan the playground network using Nmap
Any interesting information in the report?
Hint: It might be easier to use Zenmap (GUI for Nmap)

## Slide 23: Vulnerability Scanning
After scanning the network, attackers can start searching for vulnerabilities
  Manually
  Automatically
    Vulnerability scanners are automated tools that scan hosts and networks for known vulnerabilities and weaknesses
    Used together with other reconnaissance information to prepare for and plan attacks
    Credentialed and Non-Credentialed Vulnerability Scanner
Notes: Vulnerabilities:
  Common configuration errors (ex. weak/no passwords)
  Default configuration weaknesses (default accounts and passwords)
  Well-known system/application vulnerabilities ( ex. Missing OS patches or an old, vulnerable version of a web server)

## Slide 24: Vulnerability Scanner
Source: “CS635 SP2010 – Slides (Dr. Brett Tjaden - JMU)”
Notes: Scanning with credentials has opened a new frontier for security assessment. Here’s an analogy: traditional vulnerability scanning is like a mechanic evaluating a car just by looking at the outside and listening to the motor run. It’s useful but there is so much more information available by looking under the hood and plugging into the on-board diagnostics. That level of insight and internal perspective is what credentialed scanning lends to a security assessment. But even beyond the additional perspective, there are other benefits specific to control system environments that are worth noting. The number of people who use Nessus or other scanners who do not take advantage of credentialed scanning continually surprises me. Whether you are an owner/operator, an integrator, or consultant concerned with control system security, make sure you know what is available to you. Here are three reasons to get you started.

## Slide 25: Nessus
Vulnerability scanner (free for Home use)
Runs on Windows, Linux, Mac OS X, FreeBSD and Solaris
  http://www.tenable.com/products/nessus/nessus-download-agreement
Two major components:
  Server
    Vulnerability database
    Scanning engine
  Client
    Create Policy
    Run scans
    View results of a scan
Image Source: http://www.tenable.com/products/nessus
Notes: https://localhost:8834

## Slide 26: Nessus Plugins (1/2)
A plugin is a simple program which checks for a given flaw
Every audit in Tenable Nessus is coded as a plugin
There are currently over 55,000 different plugins used by Nessus, covering local and remote flaws.
Plugins are customizable – user can write new plug-ins in Nessus Attack-Scripting Language (NASL)
Image Source: http://www.tenable.com/plugins/

## Slide 27: Nessus Plugins (2/2)
Some major plugin groups:
  Backdoors
  CGI abuses
  CISCO
  Databases
  Debian Local Security Checks
  Default Unix Accounts
  Denial of Service
  DNS
  Fedora Local Security Checks
  Firewalls
  Web Servers
  Windows
All major plugin groups :http://www.tenable.com/plugins/index.php?view=all

## Slide 28: Running a Nessus Scan
Open Browser (Firefox, Safari, IE, etc.)
Connect to server (https://server_ip:8834/)
Create Policy (select which plug-ins to use)
Select target systems to scan
Run the scan
View the results

## Slide 29: Nessus Results
Vulnerabilities Severity: critical, high, medium, low or info
Need to be checked (and interpreted)
Can be used to search for or create exploits along with previous information collected:
  OS type (Windows or Unix based)
  List of open ports
  List of services and versions
  List of vulnerabilities

## Slide 30: MagicTree
Information management tool that aggregates data from a variety of other tools
Proprietary, but free
Strength is storing and sharing data
Imports tool output from Nmap, Nessus, etc.
Supports command execution from inside the tool
Supports data searching and manipulation
Included in Kali and BackTrack 5:
  Backtrack 5 – in Terminal: /pentest/reporting/magictree
  Kali – in Terminal: magictree

## Slide 31: Practice 4
Run Nmap and Nessus scans
Upload the scans in MagicTree
Interesting information in the reports?
MagicTree (Nessus and Nmap merged scans example)

## Slide 32: Sources of Information
Nessus: http://www.nessus.org/plugins/
Nmap: http://nmap.org/download
MagicTree: http://www.gremwell.com/
theHarvester: http://www.edge-security.com/theHarvester.php